## Slide 1: Pedestrian Crossing
Lesson #2
Functions and Loops
Algorithms
Messaging

## Slide 2
Alien from Planet Python needs a drill to fix his spacecraft.
You have a drill in your toolbox that you can lend him.
BUT he only speaks Python language.
How will you let him know he can borrow your drill?
Hint: from gpiozero import LED
Write the python code for Mr Martian to get the drill from the toolbox.
TOOLBOX
DRILL
Test #1

## Slide 3
Test #2
Use your blue and red LED to make the flashing lights on a patrol car
Choose any pin you wish
Wire up the circuit and write the python code to make it work

## Slide 4
Exercise 3 – Wiring a Pedestrian Crossing
PIN 14
PIN 18
GROUND
PIN 25
+VE
-VE
PIN 24

## Slide 5
TESTING OUR CIRCUIT USING THONNY SHELL
>>> from gpiozero import Buzzer
>>> buzz= Buzzer(25)
>>> buzz.on()
>>> buzz.off()
>>> buzz.blink()
Ex 3a. Turning our Buzzer on
Ex 3b. Turning it off
Ex 3c. Make it blink – 1 sec on 1 sec off
Ex 3d. Make it pulsate a number of times
>>> buzz.blink(on_time=.5, off_time=.8, n=5)

## Slide 6
THE UBIQUITOUS BUTTON
THEY MOVE THE WORLD AROUND US
THEY WORK ROUND THE CLOCK
NOTHING GETS DONE WITHOUT THEM
THEY ARE OUR INTERMEDIARIES
WE PRESS THEM ALL THE TIME, YET THEY ARE PATIENT

## Slide 7
ELEVATOR CONTROL SYSTEM
HUMANS CANNOT DIRECTLY INTERACT WITH ELEVATOR SYSTEM
INTERACTION BETWEEN HUMANS AND THE REAL WORLD VIA A COMPUTER SYSTEM
REAL WORLD
US HUMANS

## Slide 8
ELEVATOR CONTROL SYSTEM
HUMANS CANNOT DIRECTLY INTERACT WITH ELEVATOR SYSTEM
INTERACTION BETWEEN HUMANS AND THE REAL WORLD VIA A COMPUTER SYSTEM
REAL WORLD
US HUMANS

## Slide 9
Exercise 3 – Wiring a Pedestrian Crossing
PIN 14
PIN 18
GROUND
PIN 25
+VE
-VE
PIN 24

## Slide 10
TESTING OUR CIRCUIT USING THONNY SHELL
Ex 3e. Button Activating/Deactivating Buzzer
Ex 3f. Button Activating / Deactivating Red LED (Pin 14)
Can you make it Blink too?

## Slide 11
ALGORITHM FOR A PEDESTRIAN CROSSING
STARTS WITH RED
AFTER 10 SECONDS
RED GOES OFF
GREEN COMES ON
AFTER 10 SECONDS
GREEN BLINKS FIVE TIMES
AFTER 5 SECONDS
GREEN GOES OFF
RED COMES ON
Ex. 3g Pedestrian Crossing Program – Version 1
Save program as Exercise3g.py

## Slide 12
ALGORITHM FOR A PEDESTRIAN CROSSING
STARTS WITH RED
AFTER 10 SECONDS
RED GOES OFF
GREEN COMES ON
AFTER 10 SECONDS
GREEN BLINKS FIVE TIMES
BUZZER BLINKS FIVE TIMES
AFTER 5 SECONDS
GREEN GOES OFF
RED COMES ON
Ex. 3h Pedestrian Crossing Program – Version 2 – With Buzzer
Save program as Exercise3h.py

## Slide 13
ALGORITHM FOR A PEDESTRIAN CROSSING
STARTS WITH RED
AFTER 10 SECONDS
RED GOES OFF
GREEN COMES ON
AFTER 10 SECONDS
GREEN BLINKS FIVE TIMES
BUZZER BLINKS FIVE TIMES
AFTER 5 SECONDS
GREEN GOES OFF
RED COMES ON
Ex. 3j Pedestrian Crossing Program – Version 3 – Introducing a Function
Save program as Exercise3j.py

## Slide 14
ALGORITHM FOR A PEDESTRIAN CROSSING
STARTS WITH RED ON
WHEN BUTTON IS PRESSED
ACTIVATE Function greenman()
Ex. 3k Pedestrian Crossing Program – Version 4 – Add a Button
Save program as Exercise3k.py