## Slide 1
Tampines Regional Library
LearnX Community
Pi Python Introductory Course
Course Material
By
Goh Soon Seng
PLEASE DO NOT WRITE ANYTHING ON THE PAGES OF THIS BOOKLET. THANK YOU.

## Slide 2
Python Lesson – Session # 1
LIBRARIES
Machine
picozero
time
tm1637
VARIABLES
LOOPS
while True:
PYTHON RULE
Indentation
Character casing
Python Lesson – Session # 2
FUNCTIONS
CONDITIONAL STATEMENTS
if else
LOOPS
while True:
for
MESSAGING
how humans and machine communicate with each other
Python Lesson – Session # 4
REVISION & TEST
programming the lights and siren of a patrol car
INTRODUCTION TO CHATGPT
How to login to ChatGPT
Getting ChatGPT to help us code
Learning using ChatGPT
Python Lesson – Session # 3
TROUBLESHOOTING
MORE PYTHON CODING
PASSWORD
INPUT STATEMENT
Programme

## Slide 3
PIN 15
GROUND
200 OHM RESISTOR
EXERCISE #1
Wiring a Light Emitting Diode (LED)
LED
GROUND
3.3V
3.3V
+
_
GROUND
Please wire up the following circuit

## Slide 4
>>> red_led.on()
TESTING OUR CIRCUIT USING THONNY SHELL
>>> from picozero import LED
>>> red_led = LED(15)
Ex 1a. Turning our Red LED on
>>> red_led.off()
Ex 1b. Turning it off
Ex 1c. Blinking the red LED
Can you make it Blink too?

## Slide 5
Start with red led off
Wait 1 second
Turn red led on
Wait 1 second
Turn red led off
Wait 1 second
Turn red led on
Wait 1 second
Turn red led off
ALGORITHM TO CODE
ALGORITHM
CODE
RUN and save this as ex1c.py

## Slide 6
Convert
Runs once
Runs forever
Run this new program
Save it as ex1d.py
ex1c.py
while True:

## Slide 7
PIN 15
LED
EXERCISE 2 – TRAFFIC LIGHT
Please wire up this new circuit
GROUND
3.3V
3.3V
GROUND
PIN 14
PIN 13

## Slide 8
EXERCISE 2 – CONTROLLING MULTIPLE LEDs
>>> from picozero import LED
>>> red_led= LED(15)
>>> yellow_led = LED(14)
>>> green_led=LED(13)
Ex 2a. Test the Circuit. Turn each of the LEDs ON and OFF
How does a traffic light work?
Ex 2b. Turning the circuit into a Traffic Light System
How?
Green Light On
Give cars 10 seconds to cross
Green Light Off
Yellow Light On
Give 5 seconds warning
Yellow Light Off
Red Light On
Wait 10 seconds
Red Light Off
green_led.on()
sleep(10)
green_led.off()
yellow_led.on()
sleep(5)
yellow_led.off()
red_led.on()
sleep(10)
red_led.off()
Algorithm
Code
Code this in the editor
Run and save it as ex2b.py

## Slide 9
Lets create this program together
from picozero import LED
from time import sleep
red_led = LED(15)
yellow_led=LED( 14 )
green_led=LED( 13 )
Green Light On
Give cars 10 seconds to cross
Green Light Off
Yellow Light On
Give 5 seconds warning
Yellow Light Off
Red Light On
Wait 10 seconds
Red Light Off
green_led.on()
sleep(10)
green_led.off()
yellow_led.on()
sleep(5)
yellow_led.off()
red_led.on()
sleep(10)
red_led.off()
Run this program
Save program as ex2c.py
Code this in the editor

## Slide 10
Runs once
convert
Runs forever
Run the Program
Save it as ex2d.py
ex2c.py

## Slide 11
Python Lesson – Session # 2
FUNCTIONS
CONDITIONAL STATEMENTS
if else
LOOPS
while True:
for
MESSAGING
how humans and machine communicate with each other

## Slide 12
FUNCTION – A SET OF CODES WITH A NAME
ex2d.py
Run the Program
Save it as ex2e.py

## Slide 13
PIN 15
PIN 12
BUZZER
PIN 13
+
PIN 14
+
_
Look for + sign on the Buzzer
Exercise 3 – Wiring a Pedestrian Crossing

## Slide 14
TESTING OUR CIRCUIT USING THONNY SHELL
>>> from picozero import Buzzer
>>> buzzer= Buzzer(12)
>>> buzzer.on()
Ex 3a. Turning our Buzzer on
>>> buzzer.off()
Ex 3b. Turning it off
>>> from picozero import Buzzer, Button, LED
>>> buzzer= Buzzer(12)
>>> button=Button(13)
>>> red_led=LED(15)
Ex 3c. Setting up multiple sensors : our circuit has Buzzer, Button, LED
>>> button.when_pressed = buzzer.on
>>> button.when_released = buzzer.off
>>> button.when_pressed = red_led.on
>>> button.when_released = red_led.off
Let’s say we want the LED
To light up when we press the button
And off when we release the button

## Slide 15
HOW DOES A PEDESTRAIN CROSSING WORK?
RED LED IS ON / GREEN LED IS OFF
WAIT FOR 10 SECONDS
RED LED GOES OFF
GREEN LED GOES ON
GIVE 10 SECONDS FOR PEOPLE TO CROSS
GREEN LED GOES OFF
RED LED TURNS ON
Exercise 3 – Turning the circuit into a pedestrian crossing with code
from picozero import LED, Buzzer, Button
from time import sleep
red_led = LED(15)
green_led=LED(14)
buzzer=Buzzer(12)
button=Button(13)
red_led.on()
green_led.off()
convert
TO CODE
sleep(10)
red_led.off()
green_led.on()
sleep(10)
green_led.off()
red_led.on()
RUN and
Save this program as ex3c.py

## Slide 16
Exercise 3 – Turning the circuit into a pedestrian crossing with code
from picozero import LED, Buzzer, Button
from time import sleep
red_led = LED(15)
green_led=LED(14)
buzzer=Buzzer(12)
button=Button(13)
red_led.on()
green_led.off()
sleep(10)
red_led.off()
green_led.on()
sleep(10)
green_led.off()
red_led.on()
RUN ONCE
convert
RUN FOREVER
CONVERT THE
RUN ONCE PROGRAM
TO RUN FOREVER
RUN AND SAVE
PROGRAM AS
ex3d.py
ex3c.py

## Slide 17
from picozero import LED, Buzzer, Button
from time import sleep
red_led = LED(15)
green_led=LED(14)
buzzer=Buzzer(12)
button=Button(13)
red_led.on()
green_led.off()
while True:
sleep(10)
red_led.off()
green_led.on()
sleep(10)
green_led.off()
red_led.on()
How to convert this into a functon
Run program
Save it as ex3e.py
ex3d.py
Give a name for your function. Let’s call it
greenman()
def greenman():
while True:
greenman()

## Slide 18
WAIT FOR 10 SECONDS
RED LED GOES OFF
GREEN LED GOES ON
GIVE 10 SECONDS FOR PEOPLE TO CROSS
GREEN LED STARTS TO BLINK 10 TIMES (10 SECONDS)
BUZZER ALSO BLINKS 10 TIMES (10 SECONDS)
GREEN LED GOES OFF
RED LED TURNS ON
10 X
def greenman():
while True:
greenman()
ex3e.py
GREEN LED STARTS TO BLINK 10 TIMES (10 SECONDS)
BUZZER ALSO BLINKS 10 TIMES (10 SECONDS)
How?

## Slide 19
Run program
Save it as ex3f.py

## Slide 20
This program works fine.
But in the real world, it’s not practical.
Why?
We want this program to run only
when someone presses the button. How can we make use of the button
If no one wants to cross, the program will still continue to work
ex3f.py
Make this change
Run program
Save it as ex3g.py

## Slide 21
Exercise 4 – Full Fledge Pedestrian Crossing
We need another Library
to work with this device,
called a 7 Segment Display
Library: tm1637.py
CLK – Pin 19
DIO – Pin 18
PIN 15
PIN 12
PIN 13
PIN 14
PIN 11
Markings on reverse side

## Slide 22
>>> from machine import Pin
>>> import tm1637
>>> tm = tm1637.TM1637(clk=Pin(19), dio=Pin(18))
>>> tm.show(“help”)
>>> tm.number(1234)
>>> tm.temperature(24)
Exercise 4a. Display the following
PICO
95
70 Degrees Celcius
Clear the display
>>> tm.show(" " * 4)
In python " " * 4 means 4 SPACES
This will clear the display.
Make sure there is a SPACE in between the quotation marks
EXERCISE 4a – THE 7 SEGMENT DISPLAY

## Slide 23
Run program
Save as ex4b.py
COUNT DOWN DISPLAY
from machine import Pin
from time import sleep
import tm1637
tm = tm1637.TM1637(clk=Pin(19), dio=Pin(18))
for x in range(10,-1,-1):
tm.number(x)
sleep(1)
Try Counting from 0 to 20.
Refer to ex3f.py if you are not sure how to count upwards

## Slide 24
ADDING COUNTER
TO PEDESTRIAN
CROSSING
blinkblink()
Besides the green man
flashing and the buzzer
beeping
the counter will show
how much time left
for crossing
Run this amended program
Save as ex4a.py
Modify ex3c.py to add
Count down in
blinkblink()

## Slide 25
Run Program
Save as ex4b.py
Modify ex4a.py to add antispam control

## Slide 26
Python Lesson – Session # 3
TROUBLESHOTTING – 4 BASIC ERRORS
PUTTING PYTHON KNOWLEDGE TO USE
PASSWORD
INPUT STATEMENT

## Slide 27
+
+
Exercise 5 – Simple Burglar Alarm
PASSIVE INFRA-RED SENSOR - PIR
PIN 12
PIN 13
PIN 15

## Slide 28
HOW DOES A PIR WORK
Actually, it works like a Button
Remember what happens when
A button is pressed in the
Earlier example
We set the Burglar Alarm On
  at Night (ARM)
We turn it off in the morning
  (DISARM)
To DISARM a password is needed
Run program
Save as ex5a.py

## Slide 29
PIN 10
PIN 11
PIN 12
PIN 13
PIN 16
+
Exercise 5 – Enhanced Burglar Alarm
PIN 15
PASSIVE INFRA-RED SENSOR - PIR
+
_
RESET
ARM
+
+
A full fledged Burglar Alarm

## Slide 30
Ex 5b. A full fledged Burglar Alarm
A Burglar alarm should work only when it is activated
And should be deactivated when it is not required
RESET BUTTON PRESSED
ARMEDLED ON?
NO
PASS
ENTER PASSWORD
YES
PASSWORD CORRECT?
NO
TURN ARMED LED OFF
ARM BUTTON PRESSED
ARMEDLED ON?
YES
PASS
TURN ARMED LED ON
NO
WHEN MOTION IS DETECTED
ARMED LED ON?
NO
RUN ALARM
PASS
YES

## Slide 31
Run program
Save as ex5b.py
CODE FOR THE FULL FLEDGED BURGLAR ALARM
Some perculiarity to take note off

## Slide 32
Patrol Car Ex – Putting knowledge gained to use
Use your blue , red LED and a Buzzer to make a noisy flashing lights on a patrol car
Choose any pin you wish
Wire up the circuit and write the python code to make it work
HINT
Material
1 x Red LED
1 x Blue LED
1 x Buzzer
Python Code
machine and time library
while True:
Red LED on and off
Blue LED on and off
Sleep in between on and off
Use this example
Save your program
As patrolcar.py
And RUN

## Slide 33
Solution

## Slide 34
Python Lesson – Session # 4
REVISION
INTRODUCTION TO CHATGPT
Refer to Traffic Light Wiring Diagram
  How to use CHATGPT to write us the program
  Keywords in prompt
    Micropython
    Pico W
    Use picozero library
    Specify components and pin numbers
    Provide the algorithm if available