## Slide 1: Wiring an LED
Lesson #1

## Slide 2
GPIO 17
GROUND

## Slide 3
We Use the numbers inside the blue rectangles
RASPBERRY PI GPIO PIN NUMBERING SYSTEM
Pin 14
Pin 19
USB PORTS
ALWAYS ON
YOUR RIGHT

## Slide 4
INTRODUCTION TO THE THONNY INTEGRATED DEVELOPMENT ENVIRONMENT [IDE]
Click Start (Raspberry Icon)
Select Programming
Select Thonny Python IDE

## Slide 5
THE THONNY IDE HAS TWO PORTIONS TO RUN OUR PYTHON CODES
EDITOR
SHELL
Default Directory /home/pi
THE INTEGRATED DEVELOPMENT
ENVIRONMENT – I.D.E

## Slide 6
(BCM) - PIN 14
GROUND
LED
+ve ANODE
-VE CATHODE
200 OHM RESISTOR
EXERCISE #1
Wiring a Light Emitting Diode (LED)

## Slide 7
TESTING OUR CIRCUIT USING THE PYTHON LANGUAGE
>>> from gpiozero import LED
>>> red_led = LED(14)
>>> red_led.on()
Ex 1a. Turning our Red LED on
>>> red_led.off()
Ex 1b. Turning it off
>>> red_led.blink()
Ex 1c. Make it blink (1 sec on 1 sec off)
Ex 1d. Make it pulsate a number of times
>>> red_led.blink(on_time=.5, off_time=.8, n=5)

## Slide 8
Exercise 1 - WRITING OUR FIRST PYTHON PROGRAM USING THE THONNY IDE
#Library # in python means – remarks for humans
from gpiozero import LED
from time import sleep
#Setup
tf_red_led = LED(14)
#Algorithm / Logic / Sequence
tf_red_led.on()
sleep(5) #pause for 5 seconds
tf_red_led.off()
sleep(5) #pause for 5 seconds
tf_red_led.blink(on_time=.5,off_time=.5,n=5)
sleep(5) #allow 5 seconds for the blink to complete
Save this program
File -> Save [provide a programme name. E.g. Excercise1.py then click OK
Click Run or the play icon to run the program
Ex 1e. Creating our 1st Raspberry Pi Python Program
Click on the green + icon to open a new page
And type these codes into the Editor
Click the to open a new file
Type the program in the space here
Click the icon to save the program
The first time you save, you will be required to give the program a name. E.g. Exercise1
Then click the to run the program

## Slide 9
EXERCISE #2
Wiring for a Traffic Light
PIN 13
PIN 19
PIN 26
GROUND

## Slide 10
ALGORITHM FOR A TRAFFIC LIGHT SYSTEM
STARTS WITH GREEN
AFTER 10 SECONDS
GREEN GOES OFF
AMBER COMES ON
AFTER 5 SECONDS
AMBER GOES OFF
RED COMES ON
AFTER 10 SECONDS
GREEN COMES ON
Ex. 2a – Using the Logic from 1e, implement this.
Save program as Exercise2a.py