## Slide 1
Tampines Regional Library
LearnX Community
Pi Python Introductory Course
Course Material
PLEASE DO NOT WRITE ANYTHING ON THE PAGES OF THIS BOOKLET. THANK YOU.

## Slide 2
(BCM) - PIN 14
GROUND
LED
+ve ANODE
-VE CATHODE
200 OHM RESISTOR
EXERCISE #1
Wiring a Light Emitting Diode (LED)

## Slide 3
TESTING OUR CIRCUIT USING THONNY SHELL
>>> from gpiozero import LED
>>> red_led = LED(14)
>>> red_led.on()
Ex 1a. Turning our Red LED on
>>> red_led.off()
Ex 1b. Turning it off
>>> red_led.blink()
Ex 1c. Make it blink (1 sec on 1 sec off)
Ex 1d. Make it pulsate a number of times
>>> red_led.blink(on_time=.5, off_time=.8, n=5)

## Slide 4
TESTING OUR CIRCUIT USING THE THONNY EDITOR
#Library # in python means – remarks for humans
from gpiozero import LED
from time import sleep
#Setup
tf_red_led = LED(14)
#Algorithm / Logic / Sequence
tf_red_led.on()
sleep(5) #pause for 5 seconds
tf_red_led.off()
sleep(5) #pause for 5 seconds
tf_red_led.blink(on_time=.5,off_time=.5,n=5)
sleep(5) #allow 5 seconds for the blink to complete
Save this program
File -> Save [provide a programme name. E.g. Excercise1.py then click OK
Click Run or the play icon to run the program
Ex 1e. Creating our 1st Raspberry Pi Python Program
Click on the green + icon to open a new page
And type these codes into the Editor

## Slide 5
EXERCISE #2
Wiring for a Traffic Light
PIN 13
PIN 19
PIN 26
GROUND

## Slide 6
ALGORITHM FOR A TRAFFIC LIGHT SYSTEM
STARTS WITH GREEN
AFTER 10 SECONDS
GREEN GOES OFF
AMBER COMES ON
AFTER 5 SECONDS
AMBER GOES OFF
RED COMES ON
AFTER 10 SECONDS
GREEN COMES ON
Ex. 2a – Using the Logic from 1e, implement this.
Save program as Exercise2a.py

## Slide 7
Ex. 2b Traffic Light in a Loop (Exercise2b.py)
Ex. 2c Traffic Light as a Function (Exercise2c.py)
Functionalize

## Slide 8
Exercise 3 – Wiring a Pedestrian Crossing
PIN 14
PIN 18
GROUND
PIN 25
+VE
-VE
PIN 24

## Slide 9
TESTING OUR CIRCUIT USING THONNY SHELL
>>> from gpiozero import Buzzer
>>> buzz= Buzzer(25)
>>> buzz.on()
>>> buzz.off()
>>> buzz.blink()
Ex 3a. Turning our Buzzer on
Ex 3b. Turning it off
Ex 3c. Make it blink – 1 sec on 1 sec off
Ex 3d. Make it pulsate a number of times
>>> buzz.blink(on_time=.5, off_time=.8, n=5)

## Slide 10
TESTING OUR CIRCUIT USING THONNY SHELL
Ex 3e. Button Activating/Deactivating Buzzer
Ex 3f. Button Activating / Deactivating Red LED (Pin 14)
Can you make it Blink too?

## Slide 11
ALGORITHM FOR A PEDESTRIAN CROSSING
STARTS WITH RED
AFTER 10 SECONDS
RED GOES OFF
GREEN COMES ON
AFTER 10 SECONDS
GREEN BLINKS FIVE TIMES
AFTER 5 SECONDS
GREEN GOES OFF
RED COMES ON
Ex. 3g Pedestrian Crossing Program – Version 1
Save program as Exercise3g.py

## Slide 12
ALGORITHM FOR A PEDESTRIAN CROSSING
STARTS WITH RED
AFTER 10 SECONDS
RED GOES OFF
GREEN COMES ON
AFTER 10 SECONDS
GREEN BLINKS FIVE TIMES
BUZZER BLINKS FIVE TIMES
AFTER 5 SECONDS
GREEN GOES OFF
RED COMES ON
Ex. 3h Pedestrian Crossing Program – Version 2 – With Buzzer
Save program as Exercise3h.py

## Slide 13
ALGORITHM FOR A PEDESTRIAN CROSSING
STARTS WITH RED
AFTER 10 SECONDS
RED GOES OFF
GREEN COMES ON
AFTER 10 SECONDS
GREEN BLINKS FIVE TIMES
BUZZER BLINKS FIVE TIMES
AFTER 5 SECONDS
GREEN GOES OFF
RED COMES ON
Ex. 3j Pedestrian Crossing Program – Version 3 – Introducing a Function
Save program as Exercise3j.py

## Slide 14
ALGORITHM FOR A PEDESTRIAN CROSSING
STARTS WITH RED ON
WHEN BUTTON IS PRESSED
ACTIVATE Function greenman()
Ex. 3k Pedestrian Crossing Program – Version 4 – Add a Button
Save program as Exercise3k.py

## Slide 15
Exercise 4 – Wiring and Testing Count Down Display

## Slide 16
TESTING OUR CIRCUIT USING THONNY SHELL
>>> import tm1637
>>> display = tm1637.TM1637(20, 16)
>>> #20=CLK 16=DIO
>>> display.clear()
>>> display.set_values([' ', ' ', ' ', '7'])
>>> display.clear()
>>> display.set_values([' ', ' ', '8 ', '7'])
How do you display 1234
Ex 4a
Ex 4b
Ex 4c

## Slide 17
The 7 Segment Display Accepts Data as a List
A List is a collection of Data
Like this -> [‘Apple’,’Orange’,’Raspberry’,’Banana’]
We can assign as variable name to it
FruitBasket= [‘Apple’,’Orange’,’Raspberry’,’Banana’]
>>> FruitBasket= [‘Apple’,’Orange’,’Raspberry’,’Banana’]
Each it in the List has an index position, starting from 0
>>> print(FruitBasket[0] )
We can change the ‘value’ of an item in the List
e.g. we want to replace ‘Orange’ with ‘Grapes’
>>> FruitBasket[1]=‘Grapes’
>>> print(FruitBasket)

## Slide 18
Making the 7 Segment Display Library takes the display
Data as a List
[ ' ', ' ' , ' ', '9']
[ ' ', ' ' , ' ', '8']
[ ' ', ' ' , ' ', '7']
[ ' ', ' ' , ' ', '6']
[ ' ', ' ' , ' ', '5']
[ ' ', ' ' , ' ', '4']
[ ' ', ' ' , ' ', '3']
[ ' ', ' ' , ' ', '2']
[ ' ', ' ' , ' ', '1']
[ ' ', ' ' , ' ', '0']
The data to be displayed is sent to the function in the library display.set_values
At 1 seconds intervals in this case

## Slide 19
Introduction to the Python For Loop
This value is changing from 9 to 0
Create a variable
to represent this value
Give it a name counter and run it in a for loop

## Slide 20
Exercise 5 – Wiring Pedestrian Crossing with Anti Spam LED and Count Down Display

## Slide 21
Putting everything we have learned together into a full fledged pedestrian crossing
Recap our Algorithm and Code for earlier version
ALGORITHM FOR A PEDESTRIAN CROSSING
STARTS WITH RED ON
WHEN BUTTON IS PRESSED
ACTIVATE Function greenman()
Now we want to add the Countdown here as well

## Slide 22
Injecting codes for countdown display
Now we want to add the Countdown here as well

## Slide 23
Exercise 5 – Wiring Pedestrian Crossing with Anti Spam LED and Count Down Display

## Slide 24
#Library
from gpiozero import LED, Buzzer, Button
from time import sleep
from signal import pause
import tm1637
#Component Setup
green_led = LED(18)
red_led=LED(14)
anti_spam_led = LED(7)
buzz=Buzzer(25)
button=Button(24)
display=tm1637.TM1637(20,16)
#Function
def activate():
if anti_spam_led.is_lit==True:
pass
else:
anti_spam_led.on()
greenman()
def greenman():
print('Button was pressed')
sleep(10)
red_led.off()
green_led.on()
sleep(10)
for counter in range(5,-1,-1):
green_led.blink(on_time=.5,off_time=.5,n=1)
buzz.blink(on_time=.5, off_time=.5, n=1)
display.set_values([' ',' ',' ',counter])
sleep(1)
green_led.off()
red_led.on()
display.clear()
print('waiting for Button to be Pressed’)
anti_spam_led.off()
#Algorithm
red_led.on()
anti_spam_led.off()
display.clear()
print('waiting for Button to be Pressed')
button.when_pressed=activate
pause()
Adding Check for Anti Spamming Exercise3m.py

## Slide 25
EXERCISE #2
Wiring for a Traffic Light
PIN 13
PIN 19
PIN 26
GROUND

## Slide 27
Pedestrian Crossing and Traffic Light System
Co-ordinating the two systems is important
How?

## Slide 28
Suggestion for how this can be done
We take the code from Exercise3l.py
Step 1
Step 2

## Slide 29
Exercise 4 Using Motion Sensor as a Burglar Alarm

## Slide 30
Ex 4a. Motion Sensor – LED Test
Save this as Exercise4a.py
#Libraries
from gpiozero import MotionSensor, LED, Buzzer
from signal import pause
from time import sleep
#Setup Variables for Components
motion_detector = MotionSensor(4)
red_led = LED(12)
buzz = Buzzer(16)
buzz.off()
#Algorithm
motion_detector.when_motion= red_led.on
motion_detector.when_no_motion = red_led.off
pause()
Ex 4b. Motion Sensor – Buzzer Test
Save this as Exercise4b.py
#Libraries
from gpiozero import MotionSensor, LED, Buzzer
from signal import pause
from time import sleep
#Setup Variables for Componenst
motion_detector = MotionSensor(4)
red_led = LED(12)
buzz = Buzzer(16)
#Algorithm
buzz.off()
motion_detector.when_motion= buzz.on
motion_detector.when_no_motion = buzz.off
pause()

## Slide 31
Ex4c Motion Sensor – FLASHING LED AND BUZZER
Save program as Exercise4c.py
#Libraries
from gpiozero import MotionSensor, LED, Buzzer
from signal import pause
from time import sleep
#Setup Components / Variables
motion_detector = MotionSensor(4)
red_led = LED(12)
buzz = Buzzer(16)
buzz.off()
#Functions
def alarm():
buzz.blink(on_time=.5,off_time=.5,n=5)
red_led.blink(on_time=.5,off_time=.5,n=5)
sleep(5)
def alarmOff():
buzz.off()
red_led.off()
#Algorithm
motion_detector.when_motion= alarm
motion_detector.when_no_motion = alarmOff
pause()

## Slide 32
Exercise 5 Using Motion Sensor as a Burglar Alarm with Arm and Disarm Features

## Slide 33
Ex 5. BURGLAR ALARM WITH ARM AND RESET BUTTONS
#save this program as Exercise5.py
#Library
from gpiozero import MotionSensor, LED, Buzzer, Button
from signal import pause
from time import sleep
#Variables for Components
password=’12345’
motion_detector = MotionSensor(4)
red_led = LED(12)
armed_led=LED(20)
armed_led.off()
arm_button=Button(2)
reset_button=Button(21)
buzz = Buzzer(16)
buzz.off()
#Functions
def alarm():
red_led.blink(on_time=.5,off_time=.5,n=20)
buzz.blink(on_time=.5,off_time=.5,n=20)
sleep(20)
def armAlarm():
armed_led.on()
motion_detector.when_motion = alarm
def disarmAlarm():
pwd=input(‘Enter Password’)
if pwd != password:
pass
else:
armed_led.off()
buzz.off()
red_led.off()
motion_detector.when_motion = None
#Algorithm
arm_button.when_pressed = armAlarm
reset_button.when_pressed = disarmAlarm
while True:
pause()
DO Nothing