## Slide 1: Lesson #3
New Data Type - List
For Loop
Building Intelligence in Code
If Else Conditional Statements

## Slide 2
https://www.youtube.com/watch?v=8wsYT1PRjIg
Add siren to your patrol car project

## Slide 3
>>> FruitBasket= [‘Apple’,’Orange’,’Raspberry’,’Banana’]
Each item in the List has an index position, starting from 0
>>> print(FruitBasket[0] )
We can change the ‘value’ of an item in the List
e.g. we want to replace ‘Orange’ with ‘Grapes’
>>> FruitBasket[1]=‘Grapes’
>>> print(FruitBasket)
A List is a collection of Data
Like this -> [‘Apple’,’Orange’,’Raspberry’,’Banana’]
We can assign as variable name to it
Index 0 1 2 3

## Slide 4
PEDESTRIAN CROSSING – TIME LEFT COUNT DOWN DISPLAY
Please follow me closely

## Slide 5
A NEW DEVICE AND A NEW LIBRARY
Segments are controlled by the tm1637.py library
The 7 Segment Display Library

## Slide 6
The 7 Segment Display Accepts Data as a List
display.set_values([' ', ' ', '8 ', '7'])
>>> FruitBasket= [‘Apple’,’Orange’,’Raspberry’,’Banana’]
Index 0 1 2 3
0 1 2 3
0 1 2 3

## Slide 7
Exercise 4 – Wiring and Testing Count Down Display

## Slide 8
TESTING OUR CIRCUIT USING THONNY SHELL >>>
>>> import tm1637
>>> display = tm1637.TM1637(20, 16)
>>> #20=CLK 16=DIO
>>> display.clear()
>>> display.set_values([' ', ' ', ' ', '7'])
>>> display.clear()
>>> display.set_values([' ', ' ', '8 ', '7'])
How do you display 1234
Or HELP?
Ex 4a
Ex 4b
Ex 4c
Editor
Shell
File
Explorer
I.D.E Integrated Development Environment

## Slide 9
Making the 7 Segment Display Library takes the display
Data as a List
[ ' ', ' ' , ' ', '9']
[ ' ', ' ' , ' ', '8']
[ ' ', ' ' , ' ', '7']
[ ' ', ' ' , ' ', '6']
[ ' ', ' ' , ' ', '5']
[ ' ', ' ' , ' ', '4']
[ ' ', ' ' , ' ', '3']
[ ' ', ' ' , ' ', '2']
[ ' ', ' ' , ' ', '1']
[ ' ', ' ' , ' ', '0']
The data to be displayed is sent to the function in the library display.set_values
At 1 seconds intervals in this case

## Slide 10
Introduction to the Python For Loop
This value is changing from 9 to 0
Create a variable
to represent this value
We give it a name called counter
USE A for LOOP

## Slide 11
The FOR LOOP

## Slide 12
Counting from 0 to 9 in step of 1

## Slide 13
Exercise 5 – Wiring Pedestrian Crossing with Anti Spam LED and Count Down Display

## Slide 14
Putting everything we have learned together into a full fledged pedestrian crossing
Recap our Algorithm and Code for earlier version
ALGORITHM FOR A PEDESTRIAN CROSSING
STARTS WITH RED ON
WHEN BUTTON IS PRESSED
ACTIVATE Function greenman()
Now we want to add the Countdown here as well

## Slide 15
Injecting codes for countdown display
for counter in range(5,-1,-1):
green_led.blink(on_time=.5,off_time=.5,n=1)
buzz.blink(on_time=.5,off_time=.5,n=1)
sleep(1)
Now we want to add the Countdown here as well
for counter in range(5,-1,-1):
green_led.blink(on_time=.5,off_time=.5,n=1)
buzz.blink(on_time=.5,off_time=.5,n=1)
sleep(1)

## Slide 16
Exercise 5 – Wiring Pedestrian Crossing with Anti Spam LED and Count Down Display

## Slide 17
#Library
from gpiozero import LED, Buzzer, Button
from time import sleep
from signal import pause
import tm1637
#Component Setup
green_led = LED(18)
red_led=LED(14)
anti_spam_led = LED(7)
buzz=Buzzer(25)
button=Button(24)
display=tm1637.TM1637(20,16)
#Function
def activate():
if anti_spam_led.value==1:
pass
else:
anti_spam_led.on()
greenman()
def greenman():
print('Button was pressed')
sleep(10)
red_led.off()
green_led.on()
sleep(10)
for counter in range(5,-1,-1):
green_led.blink(on_time=.5,off_time=.5,n=1)
buzz.blink(on_time=.5, off_time=.5, n=1)
display.set_values([' ',' ',' ',counter])
sleep(1)
green_led.off()
red_led.on()
display.clear()
anti_spam_led.off()
print('waiting for Button to be Pressed')
#Algorithm
red_led.on()
anti_spam_led.off()
display.clear()
print('waiting for Button to be Pressed')
button.when_pressed=activate
pause()
Adding Check for Anti Spamming Exercise3m.py